## Slide 1: Evaluating characterization of fire extent and fire spread in boreal and tundra fires of Alaska from coarse and moderate resolution MODIS and VIIRS data
Tatiana Loboda, Kelley O’Neal, Qi Yang
University of Maryland

## Slide 2: The premise…
MODIS fire detections have become a “necessity” in fire management and science
MODIS is aging
VIIRS is the future but…
  largely still unknown
  challenges in access

## Slide 3: Objective
Provide background on MODIS and VIIRS instruments and data streams
Quantify the performance of active fire detection datasets over Alaskan fires 2014 – 2016
  detection rate
  earliest detection
  area burned estimate
  duration estimate
  daily area burned (fire spread)
Illustrate some differences visually
Summarize the relevance for fire management/science

## Slide 4: MODIS
http://visibleearth.nasa.gov/
Aqua
Aqua: launched May 4, 2002
Same instrument (different satellites)
Same algorithm
One combined product
Early afternoon
(~1:30 pm)
http://visibleearth.nasa.gov/
Terra
Terra: launched Dec 18, 1999
Mid-morning
(~10:30 am)

## Slide 5: VIIRS
www.noaanews.noaa.gov
Two resolutions (750, 375)
Slightly different algorithms
Two products delivered in different data streams
Suomi NPP: launched Oct 28, 2011
Early afternoon overpass (1:30 pm)

## Slide 6
Fire record in Alaska Large Fire Data Base 2014 - 2016
Chart: Area burned by ecosystem (mln acres)
| 2014.0 | 2015.0 | 2016.0
Boreal | 282188.1216 | 4443099.13 | 369617.0547
Maritime | 1404.8909 | 5853.8456 | 1742.1865
Polar | 4921.5355 | 697957.5479 | 123999.1376
~0.3
~5.1
~0.5

## Slide 7: 2014 Fire season summary
28 fire events = 288,269 acres total
By cause:
  Human 5 ; Lightning 14 ; Prescribed 9
By size:
  <100 acres 7
  100-500 acres 9
  500 – 1000 acres 6
  1000 – 10,000 acres 3
  10,000 – 50,000 acres 1
  50,000 – 100,000 acres 1
  >100,000 acres 1

## Slide 8
2014
ALFD
MODIS
VIIRS

## Slide 9
2014
MODIS Terra
MODIS Aqua
VIIRS 375
VIIRS 750

## Slide 10: 2014 active fire detection summary
14 (of 28) were flagged by at least one active fire product
  MODIS combined 14
    MODIS Terra 14
    MODIS Aqua 10
  VIIRS 750 2
  VIIRS 375 7

## Slide 11: 2014 area estimates (cumulative modeled pixels)
ALDF perimeter

## Slide 12: 2014 area estimates (cumulative modeled pixels)
MODIS Aqua active fire points

## Slide 13: 2014 area estimates (cumulative modeled pixels)
MODIS Aqua ~1 km modeled pixels

## Slide 14: 2014 area estimates (cumulative modeled pixels)
MODIS Aqua modeled burned area

## Slide 15: 2014 area estimates
Fire Name | Area burned (acres) |  |  |  |  | 
 | ALFD | MODIS Aqua | MODIS Terra | MODIS combo | VIIRS 750 | VIIRS 375
Funny River | 196,610 | 63,699 | 91,868 | 119,543 | 1,051 | 21,642
Oklahoma (DTA West) | 55,241 | 9,294 | 15,005 | 20,736 | 278 | 4,021
100 Mile Creek | 23,270 | 2,436 | 3,788 | 5,474 |  | 1,064
The Sisters | 2,622 | 1,904 | 1,914 | 2,304 |  | 
Sheep Creek 1 | 1,995 | 45 | 35 | 80 |  | 30
Tyonek | 1,906 | 193 | 396 | 590 |  | 137
Jarvis Complex | 967 |  | 246 | 246 |  | 
JBER Clunie Creek Complex | 792 |  | 116 | 116 |  | 
Noatak River | 750 | 480 | 225 | 561 |  | 
Duck Creek #3 | 573 |  | 147 | 147 |  | 37
Allman Lake | 560 | 315 | 431 | 437 |  | 
Dalton River Crossing | 403 | 72 | 64 | 127 |  | 85
Titnuk | 317 |  | 166 | 166 |  | 
Ungalik River | 214 | 128 | 44 | 131 |  | 

## Slide 16: 2014 temporal estimates
Fire Name | Earliest Detection | Estimated duration (days) |  | 
 |  | MODIS combo | VIIRS 750 | VIIRS
Funny River | MODIS | 22 | <1 | 16
Oklahoma (DTA West) | MODIS | 2 | <1 | 1
100 Mile Creek | MODIS | 16 |  | 9
The Sisters | MODIS | 2 |  | 
Tyonek | MODIS | 2 |  | <1
Noatak River | MODIS | <1 |  | 
Allman Lake | MODIS | 1 |  | 
Jarvis Complex | MODIS | <1 |  | 
Titnuk | MODIS | <1 |  | 
Duck Creek #3 | MODIS | <1 |  | <1
Ungalik River | MODIS | <1 |  | 
Dalton River Crossing | VIIRS375 | <1 |  | <1
JBER Clunie Creek Complex | MODIS | <1 |  | 
Sheep Creek 1 | VIIRS375 | <1 |  | <1

## Slide 17: Fire Spread reconstruction
ALFD perimeter

## Slide 18: Fire Spread reconstruction

## Slide 19: Fire Spread reconstruction

## Slide 20: Fire Spread reconstruction

## Slide 21: 2014 Fire Spread
MODIS
VIIRS 375

## Slide 22: 2014 Fire Spread

## Slide 23: 2014

## Slide 24: Funny river fire area burned by date
Chart: Estiamted area burned (acres)
| 37030.0 | 37031.0 | 37032.0 | 37033.0 | 37034.0 | 37035.0 | 37036.0 | 37037.0 | 37038.0 | 37039.0 | 37040.0 | 37041.0 | 37042.0 | 37043.0 | 37044.0 | 37045.0 | 37046.0 | 37047.0 | 37048.0 | 37049.0 | 37050.0 | 37051.0 | 37052.0
MODIS | 24409.1307 | 24213.4236 | 12385.5945 | 16661.7959 | 34988.8819 | 51586.6282 | 22383.5616 | 1858.3284 | 1109.3038 | 964.3026 | 544.4217 | 410.0955 | 321.1377 | 282.8858 | 302.4565 | 414.5433 | 1047.9229 | 2164.3433 | 240.1861 | 119.2035 | 43.5893 | 20.4603 | 13.3437
VIIRS 375 | 59965.5634 | 18267.4842 | 37205.7103 | 31190.3838 | 27695.2319 | 13138.1775 | 304.2357 | 233.0694 | 167.2407 | 293.5607 | 346.9354 | 197.4863 | 172.5781 | 226.8424 | 179.6948 | 176.1364 | 6672.7246

## Slide 25: 2014 total area burned by date
Chart: Estimated area burned (acres)
| 41749.0 | 41750.0 | 41751.0 | 41752.0 | 41753.0 | 41769.0 | 41770.0 | 41771.0 | 41772.0 | 41773.0 | 41774.0 | 41775.0 | 41776.0 | 41777.0 | 41778.0 | 41779.0 | 41780.0 | 41781.0 | 41782.0 | 41783.0 | 41784.0 | 41785.0 | 41786.0 | 41787.0 | 41788.0 | 41789.0 | 41790.0 | 41791.0 | 41792.0 | 41793.0 | 41794.0 | 41795.0 | 41796.0 | 41797.0 | 41798.0 | 41799.0 | 41800.0 | 41801.0 | 41802.0 | 41803.0 | 41804.0 | 41805.0 | 41806.0 | 41807.0 | 41808.0 | 41824.0 | 41825.0 | 41827.0 | 41828.0 | 41830.0 | 41862.0 | 41863.0 | 41864.0
MODIS | 509.7282 | 25.7978 | 221.5049 | 102.3015 | 103.191 | 23556.915 | 28357.0779 | 1617.2528 | 598.686 | 327.3647 | 313.1315 | 210.83 | 235.7382 | 186.8114 | 25350.3043 | 25070.0872 | 13479.7754 | 16844.1594 | 35165.9079 | 51728.0711 | 22687.7973 | 2252.4115 | 1724.0022 | 1899.249 | 1379.7355 | 1071.0519 | 3125.0875 | 1389.5208 | 883.351 | 696.5396 | 1327.2504 | 2869.7786 | 2962.2947 | 7314.1103 | 1299.6735 | 681.4167 | 410.0955 | 331.8126 | 334.4813 | 190.3697 | 122.7618 | 77.3933 | 1998.8818 | 315.8002 | 0.88958 | 568.4403 | 672.521 | 213.4987 | 2014.8942 | 1131.5432
VIIRS 375 | 35432.7813 | 16267.7129 | 432.3349 | 444.789 | 359.3895 | 283.7754 | 318.4689 | 289.1129 | 338.0396 | 279.3275 | 62594.2664 | 18524.5723 | 37453.013 | 31444.8031 | 27931.8596 | 13423.732 | 510.6178 | 553.3175 | 632.49 | 515.9552 | 594.2381 | 579.1153 | 492.8262 | 678.748 | 179.6948 | 539.0843 | 6773.2469 | 18011.2858 | 973.1983 | 198.3759 | 78.2829 | 38.2519 | 24.0186 | 16.902 | 11.5645 | 8.0062 | 1987.3173 | 0.88958 | 567.5508 | 6.227

## Slide 26: 2015 Fire season summary
334 fire events = 5,146,921 acres total
By cause:
  Human 27 ; Lightning 302 ; Prescribed 5
By size:
  <100 acres 53
  100-500 acres 49
  500 – 1000 acres 22
  1000 – 10,000 acres 106
  10,000 – 50,000 acres 79
  50,000 – 100,000 acres 15
  >100,000 acres 10

## Slide 27
2015
ALFD
MODIS
VIIRS

## Slide 28
2015
MODIS Terra
MODIS Aqua
VIIRS 375
VIIRS 750

## Slide 29: 2015 active fire detection summary
271 (of 334) were flagged by at least one active fire product
  MODIS combined 258
    MODIS Terra 255
    MODIS Aqua 245
  VIIRS 750 241
  VIIRS 375 259

## Slide 30: 2015 Area burned estimates
Chart: Area burned (acres)
| ALFD | MODIS Aqua | MODIS Terra | MODIS combo | VIIRS 750 | VIIRS 375
 | 5146921 | 2000488.637 | 2423795.9939 | 3082329.2736 | 1121270.6311 | 1290588.0336
334
245
255
258
241
259

## Slide 32: 2015 Earliest detection
MODIS 149 (55%)
VIIRS 375 73 (27%)
VIIRS 750 49 (18%)

## Slide 33: 2015 Fire event duration estimates
Chart: MODIS
Chart: MODIS
Chart: VIIRS 375

## Slide 34: 2015 Fire spread
MODIS
VIIRS 375
VIIRS 750

## Slide 35: 2015 Fire spread
MODIS
VIIRS 375
VIIRS 750

## Slide 37: 2015 complex area by date burned
Chart: Estiated burned area (acres)
| 37063.0 | 37064.0 | 37065.0 | 37066.0 | 37067.0 | 37068.0 | 37069.0 | 37070.0 | 37071.0 | 37072.0 | 37073.0 | 37074.0 | 37075.0 | 37076.0 | 37077.0 | 37078.0 | 37079.0 | 37080.0 | 37081.0 | 37082.0 | 37083.0 | 37084.0 | 37085.0 | 37086.0 | 37087.0 | 37088.0 | 37089.0 | 37090.0 | 37091.0 | 37092.0 | 37093.0 | 37094.0 | 37095.0 | 37096.0 | 37097.0 | 37098.0 | 37099.0 | 37100.0 | 37101.0 | 37102.0 | 37103.0 | 37104.0 | 37105.0 | 37106.0 | 37107.0 | 37108.0 | 37109.0 | 37110.0 | 37111.0
MODIS | 1034.5792 | 4336.6928 | 7845.1884 | 31427.9012 | 31000.9037 | 11628.5636 | 10703.4025 | 11397.2733 | 13067.0112 | 10531.7139 | 8164.5469 | 8082.7057 | 8603.1088 | 12817.9294 | 55811.2341 | 17659.0129 | 9206.2427 | 7164.6612 | 7401.289 | 12954.0348 | 10455.2102 | 6299.9914 | 4530.6208 | 4151.6605 | 3661.503 | 3939.0514 | 4043.132 | 3569.8765 | 3764.6941 | 3512.0539 | 3426.6545 | 3725.5527 | 3846.5353 | 3622.3616 | 3778.9273 | 3785.1544 | 5396.1801 | 6076.7073 | 7111.2865 | 9483.7911 | 6316.0038 | 5349.9221 | 6072.2594 | 8285.5295 | 13325.8784 | 9690.1732 | 4473.6878 | 1158.2306 | 0
VIIRS 375 | 0 | 3384.8443 | 2429.4375 | 23180.6235 | 31494.6195 | 27809.0979 | 9420.631 | 8552.4029 | 6373.8264 | 11682.8279 | 11560.9557 | 11005.859 | 11131.2895 | 13089.2507 | 22835.4673 | 50139.2848 | 6833.7382 | 6161.2172 | 5920.1416 | 6050.9096 | 11334.1133 | 15839.8259 | 6896.8982 | 5575.8749 | 5416.6404 | 3766.4733 | 3320.7947 | 3164.2289 | 2962.2947 | 2863.5516 | 2465.0206 | 2850.2079 | 2916.9263 | 2593.1199 | 2531.739 | 2514.837 | 2739.0107 | 3114.4126 | 3642.8219 | 3448.8939 | 7889.6673 | 4238.8392 | 4422.9818 | 5937.9331 | 12363.355 | 15368.3495 | 10906.2263 | 8047.1226 | 5492.2546
VIIRS 750 | 0 | 5877.4418 | 8519.4885 | 13023.4219 | 36834.7562 | 9415.2936 | 8274.8546 | 9167.1013 | 6898.6774 | 7607.6711 | 9913.4572 | 8823.7242 | 9962.384 | 16213.4486 | 35498.6101 | 21050.0842 | 9747.1061 | 6849.7506 | 6211.0336 | 5921.0312 | 4479.0252 | 4631.1431 | 4343.8094 | 4099.1754 | 4495.9272 | 3966.6283 | 4073.3777 | 4051.1382 | 4157.8876 | 4342.9198 | 4422.0922 | 4154.3293 | 4165.0042 | 4756.5736 | 4914.0289 | 5405.9655 | 6553.5211 | 7746.4452 | 9214.2489 | 10722.0836 | 11191.7808 | 9364.5876 | 7105.0595 | 9609.2216 | 17305.8504 | 35777.9376 | 1800.5059 | 1000.7753 | 0

## Slide 38: 2015 total area burned by date
Chart: Estiated burne darea (acres)

## Slide 39: 2016 Fire season summary
153 fire events = 456,485 acres total
By cause:
  Human 21 ; Lightning 132 ; Prescribed 0
By size:
  <100 acres 58
  100-500 acres 33
  500 – 1000 acres 18
  1000 – 10,000 acres 35
  10,000 – 50,000 acres 6
  50,000 – 100,000 acres 5
  >100,000 acres 0

## Slide 40
2016
ALFD
MODIS
VIIRS

## Slide 41
2016
MODIS Terra
MODIS Aqua
VIIRS 375
VIIRS 750

## Slide 42: 2016 active fire detection summary
103 (of 153) were flagged by at least one active fire product
  MODIS combined 80
    MODIS Terra 76
    MODIS Aqua 70
  VIIRS 750 73
  VIIRS 375 95

## Slide 43: 2016 Area burned estimates
Chart: Area burned (acres)
| ALFD | MODIS Aqua | MODIS Terra | MODIS combo | VIIRS 750 | VIIRS375
 | 453133.2 | 187605.9377 | 219557.6023 | 280663.1998 | 141131.6389 | 185359.0582

## Slide 45: 2016 Earliest detection
VIIRS 375 51 (50%)
MODIS 35 (34%)
VIIRS 750 17 (17%)

## Slide 46: 2016 Fire event duration estimates
Chart: MODIS
Chart: MODIS
Chart: VIIRS 375

## Slide 47
2016 Fire spread
MODIS
VIIRS 375
VIIRS 750

## Slide 48
2016 Fire spread
MODIS
VIIRS 375
VIIRS 750

## Slide 50: 2016 kuyukutuk river area by date burned
Chart: Estimated area burned (acres)
| 38141.0 | 38142.0 | 38143.0 | 38144.0 | 38145.0 | 38146.0 | 38147.0 | 38148.0 | 38149.0 | 38150.0 | 38151.0 | 38152.0 | 38153.0 | 38154.0 | 38155.0 | 38156.0 | 38157.0 | 38158.0 | 38159.0 | 38160.0 | 38161.0 | 38162.0 | 38163.0 | 38164.0 | 38165.0 | 38166.0 | 38167.0 | 38168.0 | 38169.0 | 38170.0 | 38171.0 | 38172.0 | 38173.0 | 38174.0 | 38175.0 | 38176.0 | 38177.0 | 38178.0 | 38179.0
MODIS | 1268.5382 | 1153.7827 | 1524.7367 | 7865.6487 | 4975.4098 | 2980.9759 | 463.4701 | 266.8734 | 135.2159 | 130.768 | 88.0682 | 68.4975 | 51.5955 | 43.5893 | 28.4665 | 32.9144 | 35.5831 | 22.2395 | 26.6873 | 16.902 | 15.1228 | 13.3437 | 10.6749 | 11.5645 | 7.1166 | 8.0062 | 5.3375 | 6.227 | 4.4479 | 5.3375 | 8.0062 | 3.5583 | 0.88958 | 3.5583 | 4.4479 | 3.5583 | 2.6687 | 1.7792 | 2.6687
VIIRS 375 | 752.583 | 1538.9699 | 932.2777 | 3476.4708 | 9306.765 | 5295.6578
VIIRS 750 | 913.5966 | 1496.2702 | 1572.7739 | 8795.2577 | 8533.7218

## Slide 52: 2016 Dulbi Flats fire area by date burned
Chart: Estimated area burned (acres)
| 38163.0 | 38164.0 | 38165.0 | 38166.0 | 38167.0 | 38168.0 | 38169.0 | 38170.0 | 38171.0 | 38172.0 | 38173.0 | 38174.0 | 38175.0 | 38176.0 | 38177.0 | 38178.0 | 38179.0 | 38180.0 | 38181.0 | 38182.0
MODIS | 23.129 | 3238.9535 | 1749.7999 | 1884.1262 | 6804.3821 | 4416.7548 | 2744.3481 | 1923.2676 | 1836.089 | 1190.2554 | 1037.2479 | 1202.7095 | 1382.4042 | 1783.6039 | 1813.8495 | 1756.027 | 2207.9326 | 3657.9447 | 5302.7745 | 12183.6603
VIIRS 375 | 3708.6507 | 1440.2268 | 2818.1831 | 6463.6737 | 1782.7143 | 1230.2864 | 934.0569 | 746.3559 | 611.1401 | 597.7964 | 604.913 | 644.9441 | 692.9813 | 1023.9043 | 1329.9191 | 1786.2726 | 5907.6875 | 13622.9975 | 12179.2124
VIIRS 750 | 3256.7451 | 1350.3794 | 2039.8024 | 2722.9983 | 2599.3469 | 1441.1164 | 1403.7541 | 1347.7107 | 1460.6871 | 1439.3372 | 1409.0916 | 2460.5727 | 1859.218 | 2173.2391 | 2344.038 | 3029.0131 | 5943.2706 | 9384.1583 | 10455.2102

## Slide 53: 2015 total area burned by date
Chart: Estimated area burned (acres)

## Slide 54: Summary and Take home message
No single “best” product – use the full suite
Strong predictive capability for individual fire size (if early estimates are a goal)
Highly variable estimates of duration and fire spread – potentially combining data from all products is a “MUST”