## Slide 1: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
This file contains supplementary information for the Ph.D. dissertation “Breakage of Single Droplets in 2-D Inertial Flows” by Derrick I. Ko (University of Maryland). There are droplet break-up videos corresponding to each of the figures in Sections 4.2.4 (turbulent flow) and 5.2.3 (laminar flow). With each video:
The droplet and flow parameters are presented on the upper left,
The breakage event is described on the upper right, and
Parameters of the imaging system are shown at the bottom.
The coordinate convention and shape of the flow are shown below.
Small Wake Region
(Low Pressure)
Large Wake Region
(High Pressure)
y
z
2δ = 3.175 mm
H = 12.7 mm

## Slide 2: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Initial Binary Break-up at Trailing Edge of Orifice
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 10,000 (Turbulent)
Water
Oil (CO70FG)
D = 750 μm
yinc = 3.0 mm
Figure 4.7
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
1,000 fps
10 fps (1/100th real time)
6.0 s (60 frames)
Description
This droplet extends to a moderate extent and, initially, breaks into two primary daughter droplets and no satellites. The daughters remain in the edge of the orifice jet, resulting in subsequent breakage events.

## Slide 3: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Break-up at Trailing Edge of Orifice
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 10,000 (Turbulent)
Water
Oil (CO70FG)
D = 760 μm
yinc = 3.4 mm
Figure 4.8
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
1,000 fps
10 fps (1/100th real time)
7.1 s (71 frames)
Description
This droplet widens considerably as it passes through the orifice, causing a counter-clockwise tumbling motion that creates a folded shape. A number of nodes form along the curve of the folded droplet, producing over six daughter droplets.

## Slide 4: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Break-up at Edge of Jet (Low Pressure Side)
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 14,000 (Turbulent)
Water
Oil (CO70FG)
D = 680 μm
yinc = –1.7 mm
Figure 4.9
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
1,400 fps
10 fps (1/140th real time)
7.1 s (71 frames)
Description
The droplet reaches the end of the small wake region, and slows down as it encounters the channel wall. It is at this time, as it is changing direction, that the droplet strongly extends and breaks.

## Slide 5: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Break-up at Edge of Jet (High Pressure Side)
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 10,000 (Turbulent)
Water
Oil (CO70FG)
D = 560 μm
yinc = 3.9 mm
Figure 4.10
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
1,000 fps
10 fps (1/100th real time)
8.9 s (89 frames)
Description
This droplet does not deform significantly within the orifice, but may be tumbling as it exits the orifice. It slows and breaks as it passes into the edge of the orifice jet.

## Slide 6: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Break-up in Orifice Separation Zone
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 14,000 (Turbulent)
Water
Oil (CO70FG)
D = 700 μm
yinc = –3.7 mm
compare to 4.11
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
1,400 fps
10 fps (1/140th real time)
29.4 s (294 frames)
Description
Portions of large droplets can get captured (in part) within the orifice separation zone if they approach the orifice near the channel wall. The droplet can remain in the orifice, shedding smaller droplets, over a relatively long time.

## Slide 7: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Re-entrainment into Orifice
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 14,000 (Turbulent)
Water
Oil (CO70FG)
D = 630 μm
yinc = –0.80 mm
Figure 4.12
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
1,400 fps
10 fps (1/140th real time)
30.4 s (304 frames)
Description
This droplet passes through the central region of the orifice but breaks in the upper edge of the orifice jet. The two daughters return to the orifice in the large wake region. They are pulled into the orifice separation zone and break into small daughters in the high-shear region.

## Slide 8: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Break-up and Coalescence
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 10,000 (Turbulent)
Water
Air
D = 700 μm
yinc = –0.62 mm
Figure 4.13
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
1,000 fps
10 fps (1/100th real time)
30.2 s (302 frames)
Description
This air bubble enters the orifice near the centre but translates into the lower jet edge due to the pressure across the jet. The bubble breaks in the lower edge of the orifice jet but coalesces after it enters the small wake region. The bubble eventually breaks again within the small wake region.

## Slide 9: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Simple Fracture Break-up
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 240 (Laminar)
CO70FG (μc = 0.0202 Pa-s)
Water
D = 1,170 μm
yinc = –4.1 mm
Figure 5.8
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
1,800 fps
33 fps (1/55th real time)
6.4 s (212 frames)
Description
This is a simple fracture, breaking into two primary daughter droplets and a single satellite droplet. The satellite is small, not large enough to be readily identified as an object by the image processing scripts in all frames.

## Slide 10: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Successive Fracture Break-up
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 600 (Laminar)
CO70FG (μc = 0.0202 Pa-s)
Water
D = 690 μm
yinc = –4.1 mm
Figure 5.9
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
4,510 fps
33 fps (1/137th real time)
5.8 s (192 frames)
Description
This image sequence shows a smaller droplet with the same incoming trajectory at a higher channel Reynolds number. The droplet extends the droplet more strongly, producing seven daughter droplets via successive elongative end-pinching.

## Slide 11: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Erosion Break-up
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 330 (Laminar)
CO70FG (μc = 0.0202 Pa-s)
Water
D = 930 μm
yinc = 2.7 mm
Figure 5.10
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
2,500 fps
33 fps (1/76th real time)
5.1 s (170 frames)
Description
Under conditions with relatively moderate Weber number, the fluid inside the droplet redistributes easily and limits the formation of a bulb at the trailing end. The thin tail that forms can still break into tiny droplets. In this case, two droplets are produced from this tail.

## Slide 12: Breakage of Single Droplets in 2-D Inertial Flows Supplementary Droplet Break-up Video
Combination of Fracture and Erosion
Reynolds Number:
Continuous Phase:
Dispersed Phase:
Diameter:
Incoming Trajectory:
Figure Reference:
Rech = 450 (Laminar)
CO70FG (μc = 0.0202 Pa-s)
Water
D = 730 μm
yinc = –2.2 mm
Figure 5.11
Camera:
Imaging Rate:
Playback Rate:
Duration:
Phantom v640
3,380 fps
6 fps (1/563th real time)
6.3 s (37 frames)
Description
This video shows both successive erosion and fracture mechanisms at a slower rate, allowing for a clearer view of the break-up details. The thin elongated tail produces five tiny daughter droplets before the main region of the droplet fractures successively twice from each end.